## Slide 1: Visual Output
Notes: Fotos Albrecht Schmidt

## Slide 2: Learning Goals
Understand …
  Technical parameters for visual displays
  The impact of display resolution on the user experience
  The benefits and issues of large screen setups
Know
  How 3D content can be presented
  About different technologies that can be used to create a real 3D output
Visual Output

## Slide 3: Visual Display: Screens
Display technology (e.g. LCD, LED, OLED)
Size (physical size, often the diagonal in inch, e.g. 65”)
Aspect ratio (width:height, e.g. 4:3, 16:9, or 21:9)
Resolution (number of pixel, width x height, e.g. 1920x1080)
Pixel density (how close are pixels together, size of pixels, pixels per inch, dots per inch, e.g. 320ppi)
Color depth (how many colors, per color, e.g. 8-bit / 10-bit)
Color gamut (which colors)
Mechanisms for color calibration
Refresh rate (related to images per second, 100Hz, 200Hz)
Technical Parameter
Visual Output
Spigget (CC BY-SA)
Notes: https://dot-color.com/2011/10/08/the-difference-between-color-gamut-and-bit-depth/
Spigget / CC BY-SA (https://creativecommons.org/licenses/by-sa/3.0)

## Slide 4: Visual Display: Screens
Display technology (e.g. LCD, LED, OLED)
Size (physical size, often the diagonal in inch, e.g. 65”)
Aspect ratio (width:height, e.g. 4:3, 16:9, or 21:9)
Resolution (number of pixel, width x height, e.g. 1920x1080)
Pixel density (how close are pixels together, size of pixels, pixels per inch, dots per inch, e.g. 320ppi)
Color depth (how many colors, per color, e.g. 8-bit / 10-bit)
Color gamut (which colors)
Mechanisms for color calibration
Refresh rate (related to images per second, 100Hz, 200Hz)
Technical Parameter
Visual Output
Spigget (CC BY-SA)
Notes: https://dot-color.com/2011/10/08/the-difference-between-color-gamut-and-bit-depth/
Spigget / CC BY-SA (https://creativecommons.org/licenses/by-sa/3.0)

## Slide 5: Visual Display: Screens
Aspect ration and resolution examples
Visual Output
Notes: https://dot-color.com/2011/10/08/the-difference-between-color-gamut-and-bit-depth/
https://commons.wikimedia.org/wiki/File:Cie_Chart_with_sRGB_gamut_by_spigget.png

## Slide 6: “Retina Display”
Example iPad 2 vs. iPad 3
  1024 × 768 pixel (132 ppi) vs. 2048 × 1536 pixel (264 ppi)
Angular resolution of the eye is about 1 arcminute ~ 0.02°
Assume the following viewing angle:
  60° ~ requires 3.000 pixel
  120° ~ requires 6.000 pixel
… hence 8K will be enough (with a reasonable viewing distance).
A resolution that your eyes cannot see the pixels
Visual Output
iPad2
iPad3

## Slide 7: Pixel Density
Visual Output
Traditionally 72dpi (Apple) and 96dpi (Windows)
Rapid change in the last years
Chart: 
| 2007 | 2014 | 2015
PPI | 163 | 432 | 577

## Slide 8: Pixel Density
How does it impact the user?
Visual Output
Three Tasks: image search, word counting, video analysis
16 participants, four Screen Resolutions
Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).
Notes: Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).

## Slide 9: Pixel Density
How does it impact the user?
Visual Output
Three Tasks: image search, word counting, video analysis
16 participants, four Screen Resolutions
Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).
Notes: Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).

## Slide 10: Pixel Density
How does it impact the user?
Visual Output
Measured by questionnaire
Rating mental effort on SMEQ-Scale
Rating media quality on ITU-T P.910
Measurement
Distance between eyes and tablet
Task completion time
Errors
Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).
  SMEQ
  ITU-T P.910
Notes: Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).

## Slide 11: Pixel Density
Perceived Quality
How does it impact the user? Perceived Quality
Visual Output
Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).
Perceived Effort
Notes: Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).

## Slide 12: Pixel Density
Perceived Quality
How does it impact the user? Perceived Quality
Visual Output
Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).
Perceived Effort
But…
No differences in distance
No differences in task completion time
No differences in error rate
Notes: Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).

## Slide 13: Absolute Screen Space is Useful!
It is easier to move your gaze than to bring windows to the front, move between tabs, or scroll!
Visual Output
Many tasks benefit: comparison, overview, multiple documents…
Issues with large screens:
  Finding the mouse cursor
  Moving the mouse
Practices
  Working local in one region
  Periphery for other documents
Notes: Foto Albrecht Schmidt

## Slide 14: E-Paper vs. Paper Displays, other displays
60x magnification, 10-12 pt font
Visual Output
2009
Notes: Foto Albrecht Schmidt

## Slide 15: More Visual Display Technologies
Projection
Key aspects
  Resolution
  Brightness (daylight, outdoors)
  Noise
  Projection distance
  Lens and image correction
  Connectivity
  Size and weight
E-paper Displays
Slower update rate
Black and white or few colors
Readable outdoors
Require light (like paper)
Visual Output
Notes: Foto Albrecht Schmidt

## Slide 16: 3D-Displays
Different images
One image per eye
Requirements
Visual Output
left eye right eye
Notes: Foto Albrecht Schmidt

## Slide 17: 3D View on a 2D Canvas & Displays
If we see it three dimensional we imagine it…
Expectations and experience as basis
Displaying a projection of a 3D model
“Options to visualize 3D graphics
  Create a 2D image that the user translates to 3D in his head
  Provide images (that represent a 3D model from a particular view point) for both eyes
Monocular cues (perceived with a single eye)
  Visual angle indicates how much of view object occupies
  Familiar objects perceived as constant size
  Overlapping help perception of size and depth
Everything on a 2D display is 2D!
Visual Output
https://de.wikipedia.org/wiki/Perspektive
Notes: Foto Albrecht Schmidt
  Motion parallax
  Depth from motion
  Kinetic depth effect
  Perspective
  Relative size
  Familiar size
  Absolute size
  Aerial perspective

## Slide 18: Real 3D Displays
Real physical objects
Providing a display for each eye (headset)
Overlaying images an separating them for each eye
  Time synchronized, e.g. shutter glasses
  Polarization filter on projector and glasses
  Color anaglyph systems
Autostereoscopic displays
Volumetric displays
Real 3D requires an image for each eye
Visual Output
Notes: https://en.wikipedia.org/wiki/Stereoscopy
https://commons.wikimedia.org/wiki/File:EmaginZ800.jpg
https://commons.wikimedia.org/wiki/File:Parallax_barrier_vs_lenticular_screen.svg
https://commons.wikimedia.org/wiki/File:2-punktperspektive.svg

## Slide 19: Real 3D Displays
Real physical objects
Providing a display for each eye (headset)
Overlaying images an separating them for each eye
  Time synchronized, e.g. shutter glasses
  Polarization filter on projector and glasses
  Color anaglyph systems
Autostereoscopic displays
Volumetric displays
Real 3D requires an image for each eye
Visual Output
By Alessandro Nassiri (CC BY-SA) wikimedia.org
User Psoreilly on en.wikipedia (CC BY-SA)
Notes: https://en.wikipedia.org/wiki/Stereoscopy
https://commons.wikimedia.org/wiki/File:EmaginZ800.jpg
https://commons.wikimedia.org/wiki/File:Parallax_barrier_vs_lenticular_screen.svg
https://commons.wikimedia.org/wiki/File:2-punktperspektive.svg

## Slide 20: Real 3D Displays
Real physical objects
Providing a display for each eye (headset)
Overlaying images an separating them for each eye
  Time synchronized, e.g. shutter glasses
  Polarization filter on projector and glasses
  Color anaglyph systems
Autostereoscopic displays
Volumetric displays
Real 3D requires an image for each eye
Visual Output
Snaily (CC BY-SA)
By Locafox.de (CC BY-SA) wikimedia.org
Notes: https://en.wikipedia.org/wiki/Stereoscopy
Cmglee / CC BY-SA (https://creativecommons.org/licenses/by-sa/3.0)
https://en.wikipedia.org/wiki/Anaglyph_3D
https://upload.wikimedia.org/wikipedia/commons/a/ac/3D_dusk_on_Desert.jpg
https://commons.wikimedia.org/wiki/File:Parallax_barrier_vs_lenticular_screen.svg
https://commons.wikimedia.org/wiki/File:2-punktperspektive.svg

## Slide 21: Real 3D Displays
Real physical objects
Providing a display for each eye (headset)
Overlaying images an separating them for each eye
  Time synchronized, e.g. shutter glasses
  Polarization filter on projector and glasses
  Color anaglyph systems
Autostereoscopic displays
Volumetric displays
Real 3D requires an image for each eye
Visual Output
By Cmglee (CC BY-SA) wikimedia.org
Notes: https://en.wikipedia.org/wiki/Stereoscopy
Cmglee / CC BY-SA (https://creativecommons.org/licenses/by-sa/3.0)
https://commons.wikimedia.org/wiki/File:Parallax_barrier_vs_lenticular_screen.svg
https://commons.wikimedia.org/wiki/File:2-punktperspektive.svg

## Slide 22: Real 3D Displays
Real physical objects
Providing a display for each eye (headset)
Overlaying images an separating them for each eye
  Time synchronized, e.g. shutter glasses
  Polarization filter on projector and glasses
  Color anaglyph systems
Autostereoscopic displays
Volumetric displays
Real 3D requires an image for each eye
Visual Output
Tovi Grossman, Daniel Wigdor, and Ravin Balakrishnan. 2004. Multi-finger gestural interaction with 3d volumetric displays. In Proceedings of the 17th annual ACM symposium on User interface software and technology (UIST '04). ACM, New York, NY, USA, 61-70.
Swept-screen multiplanar volumetric display
198 2-D slices
768 x 768 pixel slice resolution
100 million voxels
24 Hz volume refresh
Viewing Angle: 360º horizontal, 270º vertical
Notes: Tovi Grossman, Daniel Wigdor, and Ravin Balakrishnan. 2004. Multi-finger gestural interaction with 3d volumetric displays. In Proceedings of the 17th annual ACM symposium on User interface software and technology (UIST '04). ACM, New York, NY, USA, 61-70.

## Slide 23: Did you understand this block?
Discuss technical parameters that are relevant for visual displays?
What is the difference between a tablet screen and an e-paper display with regard to different parameters?
How does an autostereoscopic display work?
How does the shutter technology work in principle?
Why can we “see” 3D images on 2D screens?
Can you answer these questions?
Visual Output
Notes: Understand …
  Technical parameters for visual displays
  The impact of display resolution on the user experience
  The benefits and issues of large screen setups
Know
  How 3D content can be presented
  About different technologies that can be used to create a real 3D output

## Slide 24: Reference
Lischke, L., Mayer, S., Wolf, K., Sahami Shirazi, A., & Henze, N. (2015, April). Subjective and objective effects of tablet's pixel density. In Proceedings of the 33rd Annual ACM Conference on Human Factors in Computing Systems (pp. 2769-2772).
Tovi Grossman, Daniel Wigdor, and Ravin Balakrishnan. 2004. Multi-finger gestural interaction with 3d volumetric displays. In Proceedings of the 17th annual ACM symposium on User interface software and technology (UIST '04). ACM, New York, NY, USA, 61-70.
Visual Output

## Slide 25: License
This file is licensed under the Creative Commons Attribution-Share Alike 4.0 (CC BY-SA) license:
https://creativecommons.org/licenses/by-sa/4.0
Attribution: Albrecht Schmidt
For more content see: https://hci-lecture.de