## Slide 1: Olfactory Output
Taste Output
Fig. 23. Dragon vessel timepiece.

## Slide 2: Learning Goals
Understand …
  The challenges of olfactory output devices
  What parameters are used to create an artificial taste
Know
  Historic an example of using smell as information display
  The basic components and functions of an olfactory output devices
Printing and Physical Output

## Slide 3: Aromatic Output for Interaction
Humans use their sense of smell
  Is food save to eat?
  Is there danger due to a fire?
  Relationships
Unexplored medium in human computer interaction
  technical difficulties in emitting scent on demand
  chemical difficulties in creating accurate and pleasant scents
Printing and Physical Output
Joseph "Jofish" Kaye, Making scents: aromatic output for HCI, Interactions, Volume 10, Number 1 (2004), Pages 48-61
Notes: https://pixabay.com/photos/search/relationship/

## Slide 4: Incense Clocks
Historic smell output devices: Dragon vessel timepiece
Printing and Physical Output
Fig. 23. Dragon vessel timepiece. Bedini, S. A. (1963). The scent of time. A study of the use of fire and incense for time measurement in oriental countries. Transactions of the American Philosophical Society, 53(5), 1-51.

## Slide 5: Incense Clocks
timekeeping device (China, East Asia)
Clock body holds incense sticks or powdered incense
Different incenses along the body
Calibrated brining rate to measure time
Can include bells (auditory signal)
Used in homes and temples
New smell / other incense signals passage of time
…you can smell the time
Historic smell output devices
Printing and Physical Output
Bedini, S. A. (1963). The scent of time. A study of the use of fire and incense for time measurement in oriental countries. Transactions of the American Philosophical Society, 53(5), 1-51.
Fig. 23. Dragon vessel timepiece.
Notes: https://en.wikipedia.org/wiki/Incense_clock

## Slide 6: Physiology and Chemistry of Smell
A thousand different kinds of olfactory receptors in our nose,
each can sense a single kind of chemical bond in a molecule
No abstract classification of smell
  Examples: how does mint taste? It tastes like …mint
  Compared to colors: green vs. spinach colored
Rapidly acclimatized - Less than 1 minute
Human Olfactory Bandwidth… … hard to tell
  Perfumers and florist can distinguish many different smells - potentially thousands
Printing and Physical Output
Joseph "Jofish" Kaye, Making scents: aromatic output for HCI, Interactions, Volume 10, Number 1 (2004), Pages 48-61
Notes: https://en.wikipedia.org/wiki/Incense_clock

## Slide 7: Smell output
Explored in movie theaters and VR… but so far not really successful
Olfactory Icons
  Smell a “shot” fired each time you press the trigger in your game
  Ambient Notification, e.g. Smell of rose to notify you of a date or an incoming message
What information should be displayed?
An Olfactory display is useful for slowly-moving, medium-duration information or information for which an aggregate representation is slowly changing.
Printing and Physical Output
Joseph "Jofish" Kaye, Making scents: aromatic output for HCI, Interactions, Volume 10, Number 1 (2004), Pages 48-61
http://www.microfab.com/vapor-generation/aromajet

## Slide 8: Multimedia Applications with Olfaction
Printing and Physical Output
Gheorghita Ghinea and Oluwakemi Ademoye. 2012. The sweet smell of success: Enhancing multimedia applications with olfaction. ACM Trans. Multimedia Comput. Commun. Appl. 8, 1, Article 2 (January 2012), 17 pages. DOI:https://doi.org/10.1145/2071396.2071398

## Slide 9: Wearable Olfactory Output Device (Research)
Printing and Physical Output
Dobbelstein, D., Herrdum, S., & Rukzio, E. (2017, September). inScent: A wearable olfactory display as an amplification for mobile notifications. In Proceedings of the 2017 ACM International Symposium on Wearable Computers (pp. 130-137).

## Slide 10: Olfactory Output Device
Key challenges
  Creating a certain smell
  Storing and providing the smell
  Timed delivery of the smell to the user
  Neutralizing / replacing the smell
Parameters of scent delivery
  Distance
  Volume
  Speed
Printing and Physical Output
Dmitrenko, D., Vi, C. T., & Obrist, M. (2016, October). A comparison of scent-delivery devices and their meaningful use for in-car olfactory interaction. In Proceedings of the 8th International Conference on Automotive User Interfaces and Interactive Vehicular Applications (pp. 23-26).

## Slide 11: Taste Output Device (Research)
Tongue interface
  Peltier Element
  Silver electrode
Output Parameters
  Electro stimulation (polarity, frequency, 0μA to 200μA, 50Hz to 1000Hz.)
  Temperature (cooling/heating, 20°C to 35°)
Printing and Physical Output
Ranasinghe, N., Karunanayaka, K., Cheok, A. D., Fernando, O. N. N., Nii, H., & Gopalakrishnakone, P. (2011, November). Digital taste and smell communication. In Proceedings of the 6th international conference on body area networks (pp. 78-84).

## Slide 12: Did you understand this block?
What are the key challenges when creating an olfactory display?
What components do you need for outputting smell?
What parameters are relevant for olfactory output devices?
How is artificial taste created?
Give a historical example of a smell output device and explain its basic function-
Can you answer these questions?
Printing and Physical Output
Notes: Understand …
  The challenges of olfactory output devices
  What parameters are used to create an artifical taste
Know
  Historic an example of using smell as information display
  The basic components and functions of an olfactory output devices

## Slide 13: References
Joseph "Jofish" Kaye, Making scents: aromatic output for HCI, Interactions, Volume 10, Number 1 (2004), Pages 48-61
Bedini, S. A. (1963). The scent of time. A study of the use of fire and incense for time measurement in oriental countries. Transactions of the American Philosophical Society, 53(5), 1-51.
Gheorghita Ghinea and Oluwakemi Ademoye. 2012. The sweet smell of success: Enhancing multimedia applications with olfaction. ACM Trans. Multimedia Comput. Commun. Appl. 8, 1, Article 2 (January 2012), 17 pages. DOI:https://doi.org/10.1145/2071396.2071398
Dobbelstein, D., Herrdum, S., & Rukzio, E. (2017, September). inScent: A wearable olfactory display as an amplification for mobile notifications. In Proceedings of the 2017 ACM International Symposium on Wearable Computers (pp. 130-137).
Dmitrenko, D., Vi, C. T., & Obrist, M. (2016, October). A comparison of scent-delivery devices and their meaningful use for in-car olfactory interaction. In Proceedings of the 8th International Conference on Automotive User Interfaces and Interactive Vehicular Applications (pp. 23-26).
Ranasinghe, N., Karunanayaka, K., Cheok, A. D., Fernando, O. N. N., Nii, H., & Gopalakrishnakone, P. (2011, November). Digital taste and smell communication. In Proceedings of the 6th international conference on body area networks (pp. 78-84).
Printing and Physical Output

## Slide 14: License
This file is licensed under the Creative Commons Attribution-Share Alike 4.0 (CC BY-SA) license:
https://creativecommons.org/licenses/by-sa/4.0
Attribution: Albrecht Schmidt
For more content see: https://hci-lecture.de